## Slide 1: COUNTERMEASURES
Copyright © 2016 STC, UK
Notes: The previous presentations provided the background for understanding the factors that contribute to a crash occurrence and identified methods with which one can evaluate options. Module 7-2 provided some basic evaluation of alternatives considering economic aspects and system-wide evaluations. The focus of this module is to discuss methods and resources for selecting effective countermeasures and identify strategies for prioritizing countermeasures. The necessity of outcome evaluation will also be discussed.

## Slide 2: Rational vs. Pragmatic Analysis
Rational | Pragmatic
Data and analysis | Lay beliefs
Factual experience | Personal anecdotal experience
Estimates based on the effect on safety | Meeting standards means “safe”
Notes: 2
Countermeasure evaluation should be based on sound science and follow a rational approach. Only until recently we have started moving towards the direction of scientific and rational approaches in evaluating safety options based on available data and analysis, since most of prior analyses were based on lay beliefs and personal anecdotal experience. The future is described as rational because it is founded on understanding the expected consequences of actions based on factual experience and involves learning from experience. The concepts of substantive and nominal safety discussed earlier point to the need for a rational rather than pragmatic approach. As noted before, the assumption that meeting the standard is necessarily safe in not true. For example, we generally know that longer radii could improve safety but the effect of the radius on both safety and economics of the roadway could only be recently quantified though the Interactive Highway Safety Design Manual (IHSDM). It should be noted that this is not feasible using only the Green Book, since such tradeoffs are not discussed.
The rational style emphasizes estimates of the effect on safety (data and analysis), not adherence to standards based on personal experience, beliefs and intuition.

## Slide 3: Regression-to-the-Mean (RTM)
Mean
Source: FHWA
Notes: 3
The concept of the regression to the mean (discussed in Module 6) needs to be considered when evaluating potential alternative countermeasures. As noted before, there is a random crash variation and the concept of “regression to the mean” (RTM) could result in locations having a relatively high number of crashes one year, and then a drop in the next year.
This phenomenon was observed as early as 1877 in a study by Galton in which, “. . . the offspring of tall parents are generally found to be shorter than their progenitors (and vice versa)”. In this sense the heights tend to move or “regress” back toward the underlying mean, e.g. average height. The specific concern in road safety is that one should not select sites for treatment based on a high count in one year because the count will tend to “regress” back toward the mean in subsequent years.
The RTM affects both the selection of the alternative and the evaluation of its effectiveness. Alternatives chosen and implemented when the crash count is randomly high could show artificially high improvements and vice versa thus resulting in a wrong estimate of its effectiveness.

## Slide 4: High Risk Sites
Priority/emphasis areas
  Political will
  Funding sources
  Data-driven
“High risk” sites
Notes: 4
Safety improvements are typically based on determining and prioritizing high risk sites. There are several ways that such sites can be identified based both on quantitative information (data) and political will directed from top officials which can be based on a variety of factors (pragmatic as discussed above) and not necessarily based on crash data. Funding sources often tie investments to specific focus areas or activities. A careful analysis of crash data is essential in determining areas requiring attention. FHWA after reviewing the state highway safety plans has identified a series of common problems including run-off-the-road crashes, intersection-related crashes, impaired driving, occupant protection, and pedestrian safety.
The idea behind high risk site identification is to determine the exact locations where improvements can be useful and effective. For example, the knowledge that high-friction pavement can improve run of the road crashes does not mean that a DOT should implement it on all roads but rather identify locations that this could reduce these crashes. In such an approach, the high risk sites are identified and the countermeasure is applied in a targeted manner. By starting with “high risk” site identification and then determining the specific crash factors at those locations, safety investments stand a far better chance of affecting the root safety problems and reducing fatalities and serious injuries.

## Slide 5: High Risk Site Identification (1/2)
Crash numbers
Crash rates
Critical rate
Notes: Ask the students the following question prior to showing the possible approaches and try to generate some discussion.
Question: How do we identify high risk sites?
One of the simplest approaches is to use the number of crashes per year averaged over several years. The appeal of this measure lies in its simplicity, since the more crashes at a location, the generally higher level of injuries and fatalities expected. A variation on this theme would be to conduct the analysis using only mean numbers of injury and fatal crashes per year, but this does not fundamentally change the argument. A limitation of using crash frequency is the high expected number of crashes may be a primary manifestation of high traffic volumes, which may not be easily changed.
To avoid the issue of exposure inequality, one can develop crash rates per year (number of crashes divided by an exposure measure such as million vehicle miles for road sections or millions of entering vehicles for intersections or other junctions). This can also lead to not reflecting the actual ranking, since exposure measures may not be accurate and there are several other factors that can influence crash occurrence.
Some, having reflected upon this situation, have decided that a combination of crash rates and numbers should be used. This is referred to as the “number-rate” method. First a minimal number of annual crashes are selected to initially screen sites to a smaller number, and then the rate is used to generate another ranking. The difficulty is that the selection of the cut-off number for inclusion is arbitrary and there is still no assurance that the sites identified will have promise for improvement

## Slide 6: High Risk Site Identification (2/2)
HSM procedures
  SPFs
  Comparable sites
Notes: The HSM procedures also allow for the identification of the high risk sites through the use of SPFs. This approach allows for identifying the performance of the site in comparison to what is expected at similar sites. The difference between what is expected at similar sites and what is experienced at a specific site can be used to determine the potential for improvement and identify the high risk sites with promise.
The use of considering and using information about comparable sites is valuable in this scenario. Sites that seemed to hold promise using the crash frequency can be identified.

## Slide 7: High Risk Site Details
Crash Factors
  Human
  Roadway
  Vehicle
  Environmental
Collision Type
  Run-off Road
  Rear End
  Head On
  Sideswipe Same Direction
Notes: Once high risk sites are identified, the specific information regarding crash types and factors for the site should be examined. This will allow for understanding the particular performance of the site and identify specific elements that could be addressed to improve the site performance. The documentation of contributing factors is crucial in identifying potential effective countermeasures. The specific crash types can also contribute in the understanding of the potential issues and aid in the identification of the countermeasures.
These crash factors and types are generally obtained through road safety engineering studies and audits (as is discussed in Module 9). Screening by crash type should identify those types of crashes over-represented with respect to the group as a whole, thus further refining the high risk sites for identifying appropriate countermeasures. Another aspect of crash type evaluation is the potential for contrasting effects in a single countermeasure. Note that these are not all crash types that one should consider but a sample for discussion purposes.
As an example ask students: at an intersection, will the installation of a signal have a positive or negative impact on all crashes?
Answer: the signal can reduce left-turn related and crossing crashes but may increase rear end crashes, hence some types can go up while others can go down.

## Slide 8: Why Need Countermeasures?
Economic efficiency
Professional and institutional responsibility
Fairness
Notes: 8
There are three motives for considering countermeasures and those include economic efficiency, professional responsibility, and fairness.
It is imperative to consider economic efficiency to determine whether the a treatment would be cost-effective. This would provide an understanding of the effectiveness of specific countermeasures and allow for determining the potential of the countermeasure for application at each specific site. There is also professional and institutional responsibility to identify and address high risk sites. Finally, fairness to all system users is required to ensure that specific user groups are also addressed. The issue here is that typically such sites will not be routinely identified and once specific crash types and factors are identified users can be targeted to improve their safety levels.

## Slide 9: Review Methods
Engineering studies
Road Safety Audits
Road Safety Audit Reviews
  Safety improvements
Notes: Once a high risk site has been identified, some review of the site is needed to identify the various issues that can point to the reasons for the site been identified in the first place. A typical review approach is an engineering study that considers the available data and determines whether any infrastructure interventions will result in addressing the issues. These studies typically review roadway features and geometry along with crash data and attempt to correlate crashes to the features of concern. In recent years, road safety audits typically accompany engineering studies since they have the potential to provide a multidisciplinary and multimodal perspective regarding road safety. These audits (see module 9) when conducted during the design phase of the project can provide a systematic review. Road safety audit reviews are conducted at existing locations and thus are different in nature trying to identify areas, elements and road features that may contribute to a crash occurrence. The results of these reviews can be used to identify alternatives and countermeasures that could improve safety at the site in question.
The reviews could recommend actions that could be considered as immediate safety improvements indicating actions that can be implemented immediately (e.g. clearing vegetation and sight obstructions), low-cost improvements such as signing, and high-cost improvements where significant investment may be needed.
An issue to be emphasized here is the need to consider human factors and all other users in such reviews and steer away from the one-dimensional engineering only countermeasures. This is the main reason for the prevalence of road safety audits and reviews focusing on multidisciplinary and multi-modal efforts.

## Slide 10: NCHRP 500 Series Guidebooks
Notes: The NCHRP 500 series guidebooks were developed to support implementation of the AASHTO Strategic Highway Safety Plan. Each volume of the series presents information about a specific safety problem (e.g., horizontal curves, aggressive driving, teenage drivers, run-off-road crashes, etc.). Each report provides a process for addressing the problem and provides guidance in developing plans to address the issue. For each issue, several countermeasure that were identified from past research efforts are proposed and discussed. The countermeasures are classified as proven, including those that have demonstrated effectively addressing the issue; tried, including those that have been implemented but their effectiveness in not yet available; or experimental, including those that are considered and have been implemented on an experimental basis and with little or no field evaluation.

## Slide 11: Countermeasures That Work
Notes: NHTSA’s Countermeasures That Work: A Highway Safety Countermeasure Guide For State Highway Safety Offices (8th Edition, 2015) is a basic reference to assist in selecting effective, science-based traffic safety countermeasures relevant to road user crash factors. The guide summarizes major strategies and countermeasures, their effectiveness, costs, and implementation time, and provides references to research summaries and individual studies. The guide provides information on countermeasures for:
Alcohol- and drug-impaired driving;
Seat belts and child restraints;
Speeding and speed management;
Distracted and drowsy driving;
Motorcycle safety;
Young drivers;
Older drivers;
Pedestrians; and
Bicycles

## Slide 12: Proven Safety Countermeasures
Roundabouts
Corridor access management
Back-plates and retro-reflective borders
Longitudinal rumble strips and stripes on 2-lane roads
Enhanced delineation and friction on horizontal curves
Safety edges
Medians and pedestrian crossing islands in urban and suburban areas
Pedestrian hybrid beacon
Road diets
Notes: FHWA has also developed a list of proven safety countermeasures. This practice started in 2006 and every few years it is updated to reflect current thinking and research findings. The 2012 memorandum identifies these nine areas as proven countermeasures considering the latest safety research to advance a group of countermeasures that have shown great effectiveness in improving safety. FHWA also encourages safety practitioners to consider this set of countermeasures that are research-proven, but not widely applied on a national basis.
FHWA provides additional information on the effectiveness of each countermeasure in their web site (http://safety.fhwa.dot.gov/provencountermeasures/). For each countermeasure, a fact sheet is developed that provides more detailed descriptions, related research studies, and evaluations.

## Slide 13: Crash Modification Factors
Measure of safety effectiveness of a treatment or element
  CMF>1 Increase
  CMF<1 Decrease
CMF specific applications
  Crash type
  Crash severity
Notes: Crash Modification Factors (CMFs) allow for the assessment of the effectiveness of a countermeasure or treatment. The CMF is applied to the estimated crashes without treatment to estimate crashes with treatment (assuming the countermeasure of interest is implemented). It is therefore imperative to estimate the number of crashes without treatment before applying CMFs and this can be accomplished with the various methods described in the HSM module (7.1 and 7.2). As an alternative, one can estimate the crashes without treatment by computing the long-term (i.e., 5+ years) average crash frequency before treatment and thus use this as the future safety performance in the absence of changes. The Empirical Bayes method, described in the HSM, is a more rigorous method for estimating crashes without treatment as it combines information from the site of interest with information from other similar sites.
Mathematically stated, CMF = 1 - (CRF/100). For example, if a particular countermeasure is expected to reduce the number of crashes by 23% (i.e., the CRF is 23), the CMF will be 1 - (23/100) = 0.77. On the other hand, if the treatment is expected to increase the number of crashes by 23% (i.e., the CRF is -23), the CMF will be = 1 - (-23/100) = 1.23.
CMFs may apply to total crashes or to target crash types and severities. It is important to pay attention to the application range of the CMF, since several have been developed for specific crash types and severities. The user should be aware of this apply the CMF appropriately, since incorrect application may result in erroneous estimates of safety changes (a countermeasure may reduce certain crash types or severities while increasing other crash types and severities).

## Slide 14: CMF Weaknesses
Isolating specific treatments or populations
Time
Money
Multiple treatment CMFs
Notes: Research efforts have focused in isolating the effects of a a specific element and identify associated CMFs. However, countermeasures are often implemented in combination with other actions, and it is difficult to separate the effect of the countermeasure from the effect of additional actions. For example, installing a left turn phase at a signalized intersection may be accompanied by an installation of a left turn lane and thus the effect of the countermeasure may be not easily identified.
At the same time, one may have to wait for a long time to collect data regarding the effectiveness of a treatment installed in order to conduct with–without comparisons and this can also be costly. In response to these concerns researchers have tried a variety of approaches to expand our knowledge base of quantified CMFs.
The CMFs for combined treatments are not widely studied, since most past research has focused on estimating those for individual countermeasures. The current practice for many agencies is to assume that CMFs are multiplicative; this is the current method presented in the HSM and the CMF Clearinghouse.

## Slide 15: CMF Clearinghouse
www.cmfclearinghouse.org
Known CMFs
  Star rated
Notes: FHWA has developed and maintains the CMF Clearinghouse which is considered the repository of current research findings on CMFs. The webpage presents both CMFs and CRFs, or Crash Reduction Factors. The main difference between CRF and CMF is that CRF provides an estimate of the percentage reduction in crashes, while CMF is a multiplicative factor used to compute the expected number of crashes after implementing a given improvement. Both terms are presented in the Clearinghouse because both are widely used in the field of traffic safety.
The CMF clearinghouse identifies and evaluates all CMFs developed using a 5-star rating system. One-star rating indicates a low reliability on the CMF either due to limited number of sites or low number of crashes. Higher ratings provide more reliable CMFs. The database is searchable with keywords and all known CMFs are identified from a search. The applicability of CMFS to crash type and severity is also noted.
It is important to note that a CMF represents the long-term expected reduction in crashes and this estimate is based on the crash experience at a limited number of study sites; the actual reduction may vary.
Source: http://www.cmfclearinghouse.org

## Slide 16: Countermeasure Costs-Benefits
Costs
  Initial investment
  Ongoing maintenance costs
  Project life-cycle
Benefits
  Safety benefits
  Non-safety benefits
  Indirect benefits
Notes: 16
Every countermeasure has associated costs and could result in safety benefits. Obviously, for a specific site, different countermeasures will have different costs. For example, dealing with safety issues on a horizontal curve, the low-cost solution will be additional signage while the high-cost will be a new alignment. Therefore, one needs to consider the relative costs of each treatment as a function of the benefits to be derived.
Costs need to consider not only the initial investment but also the ongoing costs required over the life-cycle of the project including maintenance costs, as well as the relative long-term effectiveness of the countermeasure. One countermeasure may be just as effective as another in the short term, but less cost-effective over a longer time horizon. For example, installing speed cameras along a corridor requires significant up-front cost, but over time may be less than the cost of paying for enforcement each year along the corridor.
All benefits resulting from the countermeasure need to be accounted for developing a proper cost-benefit evaluation. Obviously crash reduction can be monetized and this is an easily estimated benefit. An issue of concern here is the proper estimation not only of the changes in the number of crashes but the estimation of the severity of those crashes. It is possible that a countermeasure may reduce the total number of crashes but affect the severity distribution. For example, placing median barriers reduces the severity of head on collisions in run of the road instances but it does affect the number of crashes (they still run off the road but now hit the barrier). Sometimes a safety countermeasure will produce benefits beyond safety benefits, e.g. mobility improvements, reduced congestion, etc. With safer, less congested roadways, indirect benefits can also occur, such as improved environmental quality and economic prosperity.

## Slide 17: Qualitative Considerations
Design standards
Tradeoffs
Familiarity
Constituent concerns
Notes: 17
A number of additional considerations may be required during the cost-benefit evaluation of a countermeasure. It is possible that untested countermeasures may conflict with existing design standards and as such agencies may tend to shy away from them. In these cases, efforts can be undertaken to establish testing procedures and determine the potential effectiveness of the countermeasure. There is a need for continuous balancing of mobility and safety needs and it is possible that these could conflict at times. It is conceivable that countermeasures perceived to conflict with other priorities may meet with resistance. As an example, the use of protected only left turn phasing could improve safety but at the expense of mobility and as such it may not be viewed favorable all the times. Proper evaluation of these tradeoffs is needed to determine the pros and cons of each option.
Another issue that can affect countermeasure implementation is the lack of familiarity with the countermeasure. In such cases proper discussion and communication with all decision-makers and stakeholders is needed to address and alleviate any such concerns. Finally, elected officials may be in favor of or oppose certain countermeasures due to the concerns of their constituents and often politicians may support or oppose a countermeasure regardless of its cost-effectiveness. This is a very difficult case to alter and public information and education efforts are important in ensuring proper dissemination and understanding of the issues.

## Slide 18: Post-Implementation Evaluation
Countermeasure effectiveness
Scientific evaluation
Notes: 18
An integral part of each countermeasure installation should be its evaluation. This is essential because it is the best mechanism for determining the effectiveness of the countermeasure. Without it, there is no information on the actual benefit of the countermeasure and no data to justify its future use. However, post-implementation evaluations are often neglected because all funds are consumed in implementing the countermeasure itself. Enough funds should be set aside to allow a proper, scientific evaluation of the countermeasures whenever possible. Lack of funds may lead to a simple comparison of the number of crashes that occurred before and after the countermeasure was applied, which may not be accurate. A proper evaluation must take into account other variables that could affect the number and/or severity of crashes, such as any change in the number of vehicles using the corridor (e.g., exposure), changes in demographics (proportion of older or younger drivers in the area), and so on.